.

| Function | OEMCode |
| --- | --- |
| Screen 1 select(e.g. Program Run screen) | 1 |
| Screen 2 select (e.g. MDI screen select) | 2 |
| e.g. Toolpath screen select | 3 |
| e.g. Positioning screen select | 4 |
| e.g. Diagnostics screen select | 5 |
| e.g. Corrections screen select | 6 |
| e.g. Tables screen select | 7 |
| Inc Inc Up | 100 |
| Inc Inc Down | 101 |
| Reset Interp | 102 |
| Jog mode toggle | 103 |
| Goto Safe Z | 104 |
| Home Z then X then Y, A, B, C - set machine coords | 105 |
| Units | 106 |
| Mach coords | 107 |
| Feed raise | 108 |
| Feed lower | 109 |
| Spindle CW, reset THC height | 110 |
| Slow Jog Up | 111 |
| Slow Jog Dn | 112 |
| Flood toggle | 113 |
| Mist toggle | 114 |
| Edit G-code | 115 |
| Zero radius DRO on X | 116 |
| Zero radius DRO on Y | 117 |
| Zero radius DRO on Z | 118 |
| Software limits | 119 |
| Touch button for Tool length offset | 120 |
| Tool Tab Save | 121 |
| Fixture Tab Save | 122 |
| Torch Enable Toggle | 123 |
| Torch Cal Zero | 124 |
| Enc Load X | 125 |
| Enc To X | 126 |
| Enc Load Y | 127 |
| Enc To Y | 128 |
| Enc Load Z | 129 |
| Enc To Z | 130 |
| Toggle Mill/Turn mode | 131 |
| Tool Path Toggle | 132 |
| Zero X Encoder | 133 |
| Zero Y Encoder | 134 |
| Zero Z Encoder | 135 |
| Tool Offset Tog | 136 |
| Fixture Off | 137 |
| Go Home | 138 |
| Part X Offset Touch | 139 |
| Part Y Offset Touch | 140 |
| Part Z Offset Touch | 141 |
| Part A Offset Touch | 142 |
| Part B Offset Touch | 143 |
| Part C Offset Touch | 144 |
| Tool X Offset Touch | 145 |
| Tool Z Offset Touch | 146 |
| Joy Throttle select | 147 |
| Touch Corr Enable Toggle | 148 |
| Auto Lim Override Toggle | 149 |
| OverRide Limits | 150 |
| SS on Act4 Toggle | 151 |
| reserved | 152 |
| reserved | 153 |
| reserved | 154 |
| Units/rev - Units/min toggle | 155 |
| Set this line as next to execute | 156 |
| Jog Follow | 157 |
| Joystick ON | 158 |
| Joystick OFF | 159 |
| Regen toolpath display | 160 |
| Zero X-Z to stock as defined in DROs (Turn) | 161 |
| Coordinate mode (G90/91) | 162 |
| Raise spindle speed | 163 |
| Lower spindle speed | 164 |
| Laser Probe Enable Toggle | 165 |
| Zero laser grid at current location | 166 |
| Z inhibit toggle | 167 |
| Ignore Tool Change toggle | 168 |
| Close current file | 169 |
| Re-load last file | 170 |
| Jog increment cycle | 171 |
| Clear error label | 172 |
| Spindle CCW toggle | 173 |
| Parallel Port Encoder3 MPG Jog Toggle | 174 |
| Cycle axis controlled by MPG 1 | 175 |
| Block Delete "switch" toggle | 176 |
| Optional Stop "switch" toggle | 177 |
| Offline toggle | 178 |
| Display Abs Machine coordinates (i.e. macnine coords ON) | 179 |
| Display Work + G92 coordinates (i.e. Machine coords OFF) | 180 |
| Display Work coords (i.e. not with G92) | 181 |
| ??? Toggle Spindle actual | 182 |
| Home X, Home Z (Turn) | 184 |
| Select X for MPG 1 | 185 |
| Select Y for MPG 1 | 186 |
| Select Z for MPG 1 | 187 |
| Select A for MPG 1 | 188 |
| Select B for MPG 1 | 189 |
| Select C for MPG 1 | 190 |
| Select Jog Increment 1 | 191 |
| Select Jog Increment 2 | 192 |
| Select Jog Increment 3 | 193 |
| Select Jog Increment 4 | 194 |
| Select Jog Increment 5 | 195 |
| Select Jog Increment 6 | 196 |
| Select Jog Increment 7 | 197 |
| Select Jog Increment 8 | 198 |
| Select Jog Increment 9 | 199 |
| Select Jog Increment 10 | 200 |
| Feed override Off | 201 |
| Feed override Jog | 202 |
| Feed override Feed | 203 |
| Jog mode Continuous (same as button 276) | 204 |
| Jog mode Step (same as button 275) | 205 |
| Joystick On | 206 |
| Joystick Off | 207 |
| Clear Z tool offset (Turn) | 208 |
| Clear X tool offset (Turn) | 209 |
| Set stock correction to Zero (Turn) | 210 |
| Home X Home Z (Turn) | 211 |
| Home X (Turn) | 212 |
| Home Z (Turn) | 213 |
| Show recent G-code files list | 214 |
| Display history | 215 |
| Load G-code | 216 |
| Tool flip toggle (Turn front/rear toolposts) | 217 |
| Z-inhibit ON | 218 |
| Z-inhibit OFF | 219 |
| Port Bit-Test Set (diagnostic) | 220 |
| Anti-dive enabled toggle | 221 |
| THC Anti-dive OFF | 222 |
| THC Anti-dive ON | 223 |
| Flood ON | 224 |
| Flood OFF | 225 |
| Mist ON | 226 |
| Mist OFF | 227 |
| Load Teach file | 228 |
| Toolpath Machine/Job toggle | 229 |
| Display Wizard selection window | 230 |
| Load the normal screens when Wizard done | 231 |
| Simple Complex screen toggle | 232 |
| Output 4 ON | 233 |
| Output 4 OFF | 234 |
| Output 5 ON | 235 |
| Output 5 OFF | 236 |
| Output 6 ON | 237 |
| Output 6 OFF | 238 |
| Set Help context | 239 |
| Def-Ref all axes | 240 |
| Tangential toggle | 241 |
| Save XYZ to G59.254 work offset | 242 |
| do G0G53 to G59.254 offset location | 243 |
| Move to G59.254 with midpoint selection | 244 |
| Toggle Jog Mode through Cont/Step/MPG as relevant | 245 |
| Force Referenced on all axes | 246 |
| CV feed toggle | 247 |
| CV feed OFF | 248 |
| CV feed ON | 249 |
| Disable movement on axis X | 250 |
| Disable movement on axis Y | 251 |
| Disable movement on axis Z | 252 |
| Disable movement on axis A | 253 |
| Disable movement on axis B | 254 |
| Disable movement on axis C | 255 |
| Machine Coordinates toggle | 256 |
| Engine OFFline | 257 |
| Engine ONline | 258 |
| Select encoder jog on axis X | 259 |
| Select encoder jog on axis Y | 260 |
| Select encoder jog on axis Z | 261 |
| Select encoder jog on axis A | 262 |
| Select encoder jog on axis B | 263 |
| Select encoder jog on axis C | 264 |
| Select Step value 1 | 265 |
| Select Step value 2 | 266 |
| Select Step value 3 | 267 |
| Select Step value 4 | 268 |
| Select Step value 5 | 269 |
| Select Step value 6 | 270 |
| Select Step value 7 | 271 |
| Select Step value 8 | 272 |
| Select Step value 9 | 273 |
| Select Step value 10 | 274 |
| Set Jog mode STEP (same as button 205) | 275 |
| Set Jog mode CONT (same as button 204) | 276 |
| Increment feedrate | 277 |
| Decrement feedrate | 278 |
| Run reverse | 279 |
| Switch to last used Wizard | 280 |
| Cycle axis controlled by MPG 2 | 281 |
| Toggle taper mode on MPG 2 | 282 |
| Toggle dual MPG flag | 283 |
| Toggle shuttle mode for MPG | 284 |
| Return to paused state | 285 |
| Remember paused state | 286 |
| Toggle override of rapid feeds | 287 |
| Crop current dwell now | 288 |
| ??? Set formlas | 289 |
| Inhibit jog of X axis | 290 |
| Inhibit jog of Y axis | 291 |
| Inhibit jog of Z axis | 292 |
| Inhibit jog of A axis | 293 |
| Inhibit jog of B axis | 294 |
| Inhibit jog of C axis | 295 |
| Do screw calibration routine | 296 |
| Unconditional crop any dwell now | 297 |
| reserved | 298 |
| Toggle bypass feed (enables value in OEM DRO 122) | 299 |
| Toggle current tool is in front toolpost | 300 |
| Code for OEMTriggers runs the macro in SetTriggerMacro | 301 |
| Cycle MPG jogging mode | 302 |
| Set MPG jogging mode = Velocity | 303 |
| Set MPG jogging mode = Velocity/Step | 304 |
| Set MPG jogging mode = do single eaxct steps | 305 |
| Set MPG jogging mode = do multiple exact steps | 306 |
| Push to jog X++ | 307 |
| Push to jog X-- | 308 |
| Push to jog Y++ | 309 |
| Push to jog Y-- | 310 |
| Push to jog Z++ | 311 |
| Push to jog Z-- | 312 |
| Push to jog A++ | 313 |
| Push to jog A-- | 314 |
| Calibrate MPGs | 315 |
| Save tool table | 316 |
| Save work offset table | 317 |
| Drag on toolpath does Zoom toggle | 318 |
| Drag on toolpath does Pan toggle | 319 |
| Display Wizard select dialog | 320 |
| Run Newfangled Wizard | 321 |
| Emergency bailout - tester use only | 322 |
| Toggle visibility of screen 50 | 323 |
| Turn mode tool touch off X axis | 324 |
| Toggle use of spindle step line to control Torch volts | 325 |
| Turn mode tool touch off Z axis | 326 |
| Select MPG jog mode | 327 |
| unknown | 328 |
| Push to Jog B++ | 329 |
| Push to Jog B-- | 330 |
| Push to Jog C++ | 331 |
| Push to Jog C-- | 332 |
| Toggle axis DROs display Dist to Go | 333 |
| Toggle X jog off | 334 |
| Toggle Y jog off | 335 |
| Toggle Z jog off | 336 |
| Toggle A jog off | 337 |
| Toggle B jog off | 338 |
| Toggle C jog off | 339 |
| Set a temporary softlimit minimum at current location | 340 |
| Set a temporary softlimit maximum at current location | 341 |
| reserved | 343 - 347 |
| Turn off display of menu bar | 348 |
| Turn on display of menu bar | 349 |
| Increment spindle speed by value not % (Turn) | 350 |
| Decrement spindle speed by value not % (Turn) | 351 |
| Jog X and A axis ++ together (foam machines) | 352 |
| Jog X and A axis -- together (foam machines) | 353 |
| Jog Y and A axis ++ together (foam machines) | 354 |
| Jog Y and A axis -- together (foam machines) | 355 |
| Cycle start | 1000 |
| Pause (Feed Hold) | 1001 |
| Rewind | 1002 |
| Stop | 1003 |
| Single | 1004 |
| Resume | 1005 |
| Edit File | 1006 |
| Zero All | 1007 |
| Zero X | 1008 |
| Zero Y | 1009 |
| Zero Z | 1010 |
| Zero A | 1011 |
| Zero B | 1012 |
| Zero C | 1013 |
| Feedrate reset | 1014 |
| Estimate Job | 1015 |
| Run from here | 1016 |
| GotoZs | 1017 |
| Coord System | 1018 |
| Verify | 1020 |
| Reset | 1021 |
| Ref X | 1022 |
| Ref Y | 1023 |
| Ref Z | 1024 |
| Ref A | 1025 |
| Ref B | 1026 |
| Ref C | 1027 |
| Joystick Toggle | 1028 |
| Softlimits Toggle | 1029 |
| Radius Tracking Toggle | 1030 |
| Jog Toggle | 1031 |

Retrieved from "http://www.machsupport.com/MachCustomizeWiki/index.php?title=OEM_Buttons"