SigmaJunmaSize+ Formula

Formula Ball screw (horizontal) Information parameters Mass of load mW Mass of table mT External Force F Coefficient of friction μ Gear ratio R Gear + coupling moment of inertia JG (null) ηG Ball screw pitch PB Ball screw diameter dB Ball screw length lB Ball screw density ρB Combined efficiency η Constants Gravity g = 9.80665 (m/s2) Circular constant π = 3.14159 Force component Frictional force FFR = μ ( mW + mT )g (N) Constant external force FC = F (N) Moment of inertia component Rotor moment of inertia JM (kg.m2) Motor option moment of inertia JMO (kg.m2) Mechanism moment of inertia (Ball screw) JMC = π ρB lB dB4 / ( 32 R 2 ) (kg.m2) Load mass moment of inertia JW = (mW + mT )( Kvn / 2π )2 (kg.m2) Load moment of inertia JL = JMC + JG + JW (kg.m2) Total load moment of inertia JA = JL + JM + JMO (kg.m2) * Kvn = PB / R (m/rev) Torque component Torque by friction TFR = FFR Kvn / ( 2π η ηG ) (N.m) Constant torque TC = FC Kvn / ( 2π η ηG ) (N.m) Torque by force from forward TFW = 0 (N.m) Torque by force from backward TBW = 0 (N.m) Sections Speed pattern section i = 1 .. n Section time ti (s) Section speed vi (m/s) Section time difference tdi = ti - ti-1 (s) Section rotation speed nMi = vi / Kvn (s-1) Section rotation speed diffrence nMdi = ( vi - vi-1 ) / Kvn (s-1) Section acceleration torque TAi = JA ( 2π nMdi / tdi ) (N.m) Section torque Ti (N.m) Normal ( nMi > 0 or nMi = 0, nMi-1 > 0 ) Ti = TAi - TC - TFW + TFR (N.m) Reverse ( nMi < 0 or nMi = 0, nMi-1 < 0 ) Ti = TAi - TC - TBW - TFR (N.m) Stopping ( nMi = 0) ¦ TC ¦ > TFR TC > 0 Ti = - TC + TFR (N.m) TC < 0 Ti = - TC - TFR (N.m) ¦ TC ¦ <= TFR Ti = 0 (N.m) n Effective torque TRMS = √ ( (Σ Ti 2 tdi ) / tn ) (N.m) i=1

Input Ball screw (horizontal) Information parameters Item Symbol Input value Unit Conversion Unit Mass of load mW 30 kg 3.000e+1 kg Mass of table mT 10 kg 1.000e+1 kg External Force F 500 N 5.000e+2 N Coefficient of friction μ 0.1 0.100 Gear ratio R 1 1.000 Gear + coupling moment of inertia JG 0.000 kg.m2 0.000 kg.m2 (null) ηG 1 1.000 Ball screw pitch PB 0.005 m 5.000e-3 m Ball screw diameter dB 0.02 m 2.000e-2 m Ball screw length lB 0.8 m 0.800 m Ball screw density ρB 7870.000 kg/m3 7.870e+3 kg/m3 Combined efficiency η 1 1.000

Speed Section i End time tin (s) Reached speed vin (m/s) End time ti (s) Speed vi (m/s) 1 0.400 0.100 0.400 0.100 2 1.400 0.100 1.400 0.100 3 1.900 0.000 1.900 0.000 4 4.000 0.000 4.000 0.000

Motor specification : SGM-02A*1 Item Symbol value Unit Rated output PMRTD 0.200 kW Rated torque TMRTD 0.637 N.m Maximum torque TMMAX 1.910 N.m Rated rotation speed nMRTD 3000 min-1 Maximum rotation speed nMMAX 4500 min-1 Rotor moment of inertia JM 1.230e-5 kg.m2 Motor option moment of inertia JMO 0.000 kg.m2 Allowable moment of inertia ratio RJLM 3.000e+1

Result Force component Frictional force FFR = μ ( mW + mT )g = 3.923e+1 (N) Constant external force FC = F = 5.000e+2 (N) Moment of inertia component Mechanism moment of inertia (Ball screw) JMC = π ρB lB dB4 / ( 32 R 2 ) = 9.890e-5 (kg.m2) Load mass moment of inertia JW = (mW + mT )( Kvn / 2π )2 = 2.533e-5 (kg.m2) Load moment of inertia JL = JMC + JG + JW = 1.242e-4 (kg.m2) Total load moment of inertia JA = JL + JM + JMO = 1.365e-4 (kg.m2) * Kvn = PB / R = 5.000e-3 (m/rev) Torque component Torque by friction TFR = FFR Kvn / ( 2π η ηG ) = 3.122e-2 (N.m) Constant torque TC = FC Kvn / ( 2π η ηG ) = 0.398 (N.m) Torque by force from forward TFW = 0.000 (N.m) Torque by force from backward TBW = 0.000 (N.m) Required maximum torque TMAX = 0.401 (N.m) Effective torque TRMS = 0.367 (N.m) Required maximum rotation speed nMAX = 1.200e+3 (min-1) Moment of inertia ratio (load/rotor) JL/JM = 1.010e+1 Duty(Effective torque/Rated torque) RTRMS = 57.633 (%) Torque ratio (Peak torque/Instantaneous peak torque) RTMAX = 20.994 (%)

Section time, rotation speed, torque conversions Section i End time ti (s) Rotation speed nMi (s-1) Rotation speed 60nMi (min-1) Section torque Ti (N.m) 1 0.400 2.000e+1 1.200e+3 -0.324 2 1.400 2.000e+1 1.200e+3 -0.367 3 1.900 0.000 0.000 -0.401 4 4.000 0.000 0.000 -0.367

Motor sizing condition Maximum torque ≥ Required maximum torque Rated torque ≥ Effective torque Rated torque ≥ ¦ Constant torque ¦ + frictional torque Maximum rotation speed ≥ Required maximum rotation speed

(C) YASKAWA ELECTRIC CORPORATION