Tips for ordering drill chuck arbors:
Most often, a drill chuck arbor has a longer end that is either a straight shank or a male Morse Taper to fit into a drill press. The other, shorter end of the arbor is a male Jacobs taper to fit into a drill chuck. If a drill press has a non-removable male spindle, the taper is usually 33 Jacobs Taper.

JACOBS KÚPOK

JACOBS     Nagy      Kicsi

Kúp       átmérő     átmérő       Hosz

---------------------------------------

0        .25000"    .22844     .43750

1        .38400     .33341     .65625

2        .55900     .48764     .87500

2 short    .54880     .48764     .75000

3        .81100     .74610    1.21875

4       1.12400    1.03720    1.65625

5       1.41300    1.31611    1.87500

6        .67600     .62409    1.00000

33        .62401     .56051    1.00000

| JACOBS | Nagy | Kicsi |  |
| --- | --- | --- | --- |
| kúp | átmérő " | átmérő " | Hosz " |
| 0 | 0,25000 | 0,22844 | 0,43750 |
| 1 | 0,38400 | 0,33341 | 0,65625 |
| 2 | 0,55900 | 0,48764 | 0,87500 |
| 2 rövid | 0,54880 | 0,48764 | 0,75000 |
| 3 | 0,81100 | 0,74610 | 1,21875 |
| 4 | 1,12400 | 1,03720 | 1,65625 |
| 5 | 1,41300 | 1,31611 | 1,87500 |
| 6 | 0,67600 | 0,62409 | 1,00000 |
| 33 | 0,62401 | 0,56051 | 1,00000 |

MORSE TAPERS

LARGE      SMALL

MORSE     DIAMETER   DIAMETER

TAPER#      (A)        (B)       LENGTH

---------------------------------------

0        .36510"    .25200     1-15/16

1        .47500     .36900     2-1/16

2        .70000     .57200     2-1/2

3        .93800     .77800     3-1/16

4       1.23100    1.02000     3-7/8

4-1/2     1.50000    1.26600     4-5/16

5       1.74800    1.47500     4-15/16

6       2.49400    2.11600     7

7       3.27000    2.75000     9-1/2

| MORSE | Nagy | Kicsi |  |
| --- | --- | --- | --- |
| kúp | átmérő " A | átmérő " B | Hosz " |
| 0 | 0,36510 | 0,25200 | 1-15/16 |
| 1 | 0,47500 | 0,36900 | 2-1/16 |
| 2 | 0,70000 | 0,57200 | 2-1/2 |
| 3 | 0,93800 | 0,77800 | 3-1/16 |
| 4 | 1,23100 | 1,02000 | 3-7/8 |
| 4-1/2 | 1,50000 | 1,26600 | 4-5/16 |
| 5 | 1,74800 | 1,47500 | 4-15/16 |
| 6 | 2,49400 | 2,11600 | 7 |
| 7 | 3,27000 | 2,75000 | 9-1/2 |

BROWN & SHARP TAPERS

LARGE      SMALL

B+S      DIAMETER   DIAMETER

TAPER#      (A)        (B)       LENGTH

---------------------------------------

1        .23922"    .20000       15/16

2        .29968     .25000     1-3/16

3        .37525     .31250     1-1/2

4        .40233     .35000     1-1/4

5        .52315     .45000     1-3/4

6        .59961     .50000     2-3/8

7        .72537     .60000     3

8        .89873     .75000     3-9/16

9       1.06705     .90010     4

10       1.28927    1.04465     5-11/16

11       1.53176    1.24995     6-3/4

12       1.79681    1.50010     7-1/8

13       2.07310    1.75005     7-3/4

14       2.34375    2.00000     8-1/4

15       2.61458    2.25000     8-3/4

---------------------------------------

| B+S | Nagy | Kicsi |  |
| --- | --- | --- | --- |
| kúp | átmérő " A | átmérő " B | Hosz " |
| 1 | 0,23922 | 0,20000 | 15/16 |
| 2 | 0,29968 | 0,25000 | 1-3/16 |
| 3 | 0,37525 | 0,31250 | 1-1/2 |
| 4 | 0,40233 | 0,35000 | 1-1/4 |
| 5 | 0,52315 | 0,45000 | 1-3/4 |
| 6 | 0,59961 | 0,50000 | 2-3/8 |
| 7 | 0,72537 | 0,60000 | 3 |
| 8 | 0,89873 | 0,75000 | 3-9/16 |
| 9 | 1,06705 | 0,90010 | 4 |
| 10 | 1,28927 | 1,04465 | 5-11/16 |

# Morse Taper sizes

Different Morse tapers have easily distinguished sizes.

Measure at the big end (ie, the open hole), in inches:

- #0 is 0.356

- #1 is 0.475

- #2 is 0.700

- #3 is 0.938

- #4 is 1.231,

- #5 is 1.748

- #6 is 2.494

- #7 is 3.270

| Principal dimensions of Morse Taper Shank in accordance with BS1660, 1972 / ISO 296/DIN 228 |
| --- |
| MORSE TAPER No. A mm B mm C mm D mm E mm TAPER per mm on dia. 1 12.065 62.0 65.5 5.2 5 0.04988 2 17.780 75.0 80.0 6.3 6 0.04995 3 23.825 94.0 99.0 7.9 7 0.05020 4 31.267 117.5 124.0 11.9 8 0.05194 5 44.399 149.5 156.0 15.9 10 0.05263 |  |

# Machine taper

### From Wikipedia, the free encyclopedia

Jump to: navigation, search

A machine taper is a system for securing cutting bits and other accessories to a machine tool's powered rotating spindle. Machine tool operators must be able to install or remove such components quickly and easily. A lathe, for example, has a rotating spindle in its headstock, to which one may want to mount a spur drive or work in a collet. Another example is a drill press, to which an operator may want to mount a bit directly, or using a drill chuck. Virtually all milling machines, from the oldest, manual machines up to the most modern CNC machines utilize tooling that is piloted on a tapered surface.

Several options exist: (1) a threaded spindle, into/onto which accessories are screwed, (2) a permanently mounted chuck (as with some drill presses), or (3) a taper mount.

This simple, low-cost, and versatile tool mounting system involves (A) tool bits or holders with gradually tapered shanks, and (B) a matching hollowed-out spindle. Tools are simply slipped onto or into the spindle; the pressure of the spindle against the workpiece drives the tapered shank tightly into the tapered hole. The friction across the entire surface area of the interface provides a surprisingly large amount of torque transmission, so that splines or keys are not required.

Contents [hide] 1 Method of specification; overview of families 2 Details of use 3 Families of tapers 3.1 Morse 3.1.1 Morse Taper Dimensions 3.2 Brown & Sharpe 3.3 R8 3.4 Jacobs 3.5 Jarno 3.6 NMTB Tapers 3.7 NT 40 (int40) 3.8 NT 50 (int50) 4 External links

## [edit] Method of specification; overview of families

There are multiple different standard tapers, each differing in (a) the diameter at the small end of the truncated cone ("the minor diameter"); (b) the diameter at the large end of the truncated cone ("the major diameter"); (c) the axial distance between the two ends of the truncated cone.

The standards are grouped into families. One of the most widely used is the "Morse taper", which comes in 8 varieties, from "Morse 0" at 59.4 mm (2.34 inches) from end to end - to "Morse 7" at 295.3 mm (11.625 inches) from end to end.

It is noteworthy that even though one could design a family of tapers that all have the same included angle, the actual families of tapers in existence do not exhibit this design feature. Morse tapers, for example, taper at anywhere from 0.04988 inches of diameter per inch of length (for the Morse 1) to 0.05262 inches of diameter per inch of length (for the Morse 5).

One of the first uses of tapers was to mount drill bits directly to machine tools, although later drill chucks were invented that mounted to machine tools and in turn held non-tapered drill bits.

## [edit] Details of use

Bits or accessories are inserted into a tapered receptacle and pushed or twisted into place. They are then held by friction.

Tapered shanks "stick" in tapers best when both the shank and the receptacle are clean. Shanks can be wiped clean, but receptacles, being deep and inaccessible, are best cleaned with a specialized taper cleaning tool which is inserted, twisted, and removed.

Tapered shank tools are removed from tapered receptacles either by inserting a drift punch axially from behind, and tapping the tapered shank tool out of the receptacle, or - if the tapered shank tool is so designed - inserting a wedge shaped block of metal called a "drift" into a rectangular shaped cross hole through the shank, and tapped. As the cross section of the drift gets larger when the drift is pushed further in, the result is that the drift, bearing against the foremost edge of the tang receptacle, pulls the tapered tang out.

## [edit] Families of tapers

### [edit] Morse

Morse Taper #2 (MT2)

The Morse Taper was invented by Stephen A. Morse (also the inventor of the twist drill) circa 1864. Since then it has evolved to encompass smaller and larger sizes and has been adopted as a standard by numerous organizations including ISO as ISO 296:1991 Machine Tools -- Self-Holding Tapers for Tools Shanks, and DIN as DIN 228-1:1987-05 Morse tapers and metric tapers; taper shanks.

Morse Tapers come in eight sizes identified by number between 0 and 7. Often this is abbreviated as MT followed by a digit, for example a Morse taper number 4 would be MT4. The MT2 taper is the size most often found in drill presses up to 1/2" capacity.

Morse tapers can have two types of ends:

- tang (illustrated) to facilitate removal with a drift

- threaded to be held in place with a draw bar

The taper itself is roughly 5/8" per foot, but exact ratios and dimensions for the various sizes of tang type tapers are given below.

#### [edit] Morse Taper Dimensions

| Morse Taper | Taper | A | B (max) | C (max) | D (max) | E(max) | F | G | H | J | K |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 19.212:1 | 9.045 | 56.5 | 59.5 | 10.5 | 6 | 4 | 1 | 3 | 3.9 | 1°29'27" |
| 1 | 20.047:1 | 12.065 | 62 | 65.5 | 13.5 | 8.7 | 5 | 1.2 | 3.5 | 5.2 | 1°25'43" |
| 2 | 20.020:1 | 17.780 | 75 | 80 | 16 | 13.5 | 6 | 1.6 | 5 | 6.3 | 1°25'50" |
| 3 | 19.922:1 | 23.825 | 94 | 99 | 20 | 18.5 | 7 | 2 | 5 | 7.9 | 1°26'16" |
| 4 | 19.254:1 | 31.267 | 117.5 | 124 | 24 | 24.5 | 8 | 2.5 | 6.5 | 11.9 | 1°29'15" |
| 5 | 19.002:1 | 44.399 | 149.5 | 156 | 29 | 35.7 | 10 | 3 | 6.5 | 15.9 | 1°30'26" |
| 6 | 19.180:1 | 63.348 | 210 | 218 | 40 | 51 | 13 | 4 | 8 | 19 | 1°29'36" |
| 7 | 19.231:1 | 83.058 | 285.75 | 294.1 | 34.9 | - | - | 19.05 | - | 19 | 1°29'22" |
| Morse Taper Dimensions (mm) |

### [edit] Brown & Sharpe

Brown & Sharpe tapers, standardized by the eponymous company, are an alternative to the more-commonly seen Morse taper. Like the Morse, these have a series of sizes, from 1 to 18, with 7, 9 and 11 being the most common. Actual taper on these is within a close range of .500" per foot.

### [edit] R8

collets with R8 taper

This taper was designed by Bridgeport Machines Inc. for use in their milling machines. It is used with a drawbar extending up through the spindle to the top of the machine to prevent the collet from falling from the spindle when lateral forces are encountered. The collet, which is inserted into the taper, has a precision hole in one end for holding a cutting tool and is threaded for a drawbar on other end. They are also keyed (see image) to prevent rotation during insertion and removal. However, cutting torques are transferred through friction at the taper, not through the key. The drawbar thread is typically 7/16"-20tpi (UNF).

The cutting tool is placed in the collet, the collet placed into the taper, and the drawbar is tightened into the top of the collet from above the spindle. The collet has a groove to engage a key in the spindle to keep the collet from spinning inside the taper and to aid in the installation and removal of the collet. The angle of the cone is typically 16 degrees and 51 minutes (i.e. 16.85 degrees) with an OD of 1.25" (source, Bridgeport Manufacturer).

### [edit] Jacobs

The Jacobs Taper (abbreviated JT) is commonly used to secure drill press chucks to an arbor.

| Taper | Small End | Big End | Length |
| --- | --- | --- | --- |
|  | mm | inch | mm | inch | mm | inch |
| 0 | 5.80 | 0.2284 | 6.35 | 0.2500 | 11.11 | 0.4375 |
| 1 | 8.47 | 0.3334 | 9.75 | 0.3840 | 16.67 | 0.6563 |
| 2 | 12.39 | 0.4876 | 14.20 | 0.5590 | 22.23 | 0.8750 |
| 2 Short | 12.39 | 0.4876 | 13.94 | 0.5488 | 19.05 | 0.7500 |
| 3 | 18.95 | 0.7461 | 20.60 | 0.8110 | 30.96 | 1.2188 |
| 4 | 26.34 | 1.0372 | 28.55 | 1.1240 | 42.07 | 1.6563 |
| 5 | 33.43 | 1.3161 | 35.89 | 1.4130 | 47.63 | 1.8750 |
| 6 | 15.85 | 0.6241 | 17.17 | 0.6760 | 25.40 | 1.0000 |
| 33 | 14.23 | 0.5604 | 15.85 | 0.6240 | 25.40 | 1.0000 |

### [edit] Jarno

Jarno tapers range from a Number 2 to a Number 20. The diameter of the big end in inches is always the taper size divided by 8, the small end is always the taper size divided by 10 and the length is the taper size divided by 2. For example a Jarno #7 measures 0.875" (7/8) across the big end. The small end measures 0.700" (7/10) and the length is 3.5" (7/2).

The system was invented by Oscar J. Beale of Brown & Sharpe.

### [edit] NMTB Tapers

The National Machine Tool Builders Association (now called the Association for Manufacturing Technology) laid down standards for machine tool design, among other things: the taper used on CNC (Computer Numerically Controlled) milling machines.

The taper is variously referred to as NMTB, NMT or NT. Essentially this defines a taper of 3.500 inches per foot, or 16.2602047... degrees. All NMTB Tooling has this taper but the tooling comes in different sizes. NMTB-25, 30, 35, 40, 45, 50 and 60. With the 40 taper being the most common by far.

CAT and BT tooling use this same taper.

The goal of the taper is to allow a quick and easy change between different tools (either automatically or by hand) and still keep it tight and centered while using it. The spindle on the machine tool is built with a female taper and drawbar. Each individual tool must be fitted with a male taper and the proper adapter for the drawbar.